stereo
out
2x
cinch stereo inputs
DIN
DIN
reserved
220V
mix
MIDI in
(out unsused)
GT-2
mini
220V
in
phones out
Ketron
SD-2
stereo out
MIDI
through
MIDI out
channel 1
MIDI
through
Triac
relais
power
sensor
MIDI in
Keyboard
Sensor
power
slaves
right: channel 1
left: channel 2
foot: channel 3
Tx3
DIN
DIN
Rx2
Display
button
ext. switch 1
Rx3
Rx3
Tx2
Controller
ext. Switch 2
or expression
pedal
Sub-D connector
Foot Pedal
exit
enter
modulation
pitch bend
L
R
L
R
L
R
volume knob

---
Diodenmatrix Fußpedal
Diodenmatrix Fußpedal
Sub-D Stift-Nr.
G8 violett
8
G7 blau
7
G6 gelb
6
G5 braun
5
G4 weiß
4
G3 grau-rosa
3
G2 grau
2
G1 schwarz
1
A12 rot-
schwarz
A13 rot
11
12
14
15
R12 grün-
braun
R13 grün
A14 rosa
A = Arbeitskontakt
R = Ruhekontakt
13
Reserve:
R14 grün-weiß
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

---
220
220
300
220
300
diode matrix rows
A12 red-black
1k
R12 green-
brown
1k
220
A13 red
R13 green
A14 light red
R14 green-
white
contrst.
10..20k
G1 black
G2 grey
G3 grey-lght.rd.
G4 white
G5 brown
G6 yellow
G7 blue
G8 violet
diode matrix columns
470n
68k
Gnd
switch
violet
ext. switch 2
/ expression
white
grey
blue
black-
white
int. red switch (enter)
100n
470n
470n
22k
black
black
int. black switch (exit)
AV2020
LCD
16 LED -
15 LED +
14 D7
13 D6
12 D5
11 D4
10 D3
9 D2
8 D1
7 D0
6 Enable
5 R/W
4 Funct. Select
3 LCD Drive
2 +5V
1 Gnd
Arduino
Mega 2560
22
23
24
25
26
27
 14 15 16 17 18 19
Tx3 Rx3 Tx2 Rx2 Tx1 Rx1
+5V
53
51
52
50
        Gnd +5V A0 A1 A2 A3 A7
28
40
30
32
42
34
36
44
38
29
31
33
35
37
39
41
43
+5V Gnd
10..20k
10..20k
pitch bnd.
modulat.
orange
yellow
1k
1k
1k
1k
PC817
5 4
5 4
220
5 4
PC817
5 4
volume
10k

---
TLE2072
7809
+9V
Netzteil
mit
Brücken-gleichrichter
+9V
left
right
20k
20k
GT2 x 1
ext. x 2
ext. x 2
x 1
x 2
x 2
20k
+
4,7uF
+
4,7uF
Audio Mixer
Input fg = 3,4 Hz
1/2
TLE 2072
-
+
20k
+
4,7uF
+
4,7uF
+
4,7uF
+
4,7uF
+
4,7uF
+
4,7uF
5k
5k
+
4,7uF
+
4,7uF
0,1uF
+
1000uF
1/2
TLE 2072
-
+